## Slide 1: CUDA OPTIMIZATION, PART 1
NVIDIA Corporation

## Slide 2: OUTLINE
Kernel optimizations
Launch configuration (use lots of threads)
Part 2 (next session):
Global memory throughput (use memory efficiently)
Shared memory access
Most concepts in this presentation apply to any language or API on NVIDIA GPUs
Architecture:
Kepler/Maxwell/Pascal/Volta

## Slide 3: KEPLER CC 3.5 SM (GK110)
3
“SMX” (enhanced SM) SIMD processor
192 SP(single precision) units (“cores”)
64 DP (double precision) units
LD/ST units,
64K registers
4 warp scheduler
Each warp scheduler is dual-issue capable
K20: 13 SMX’s, 5GB
K20X: 14 SMX’s, 6GB
K40: 15 SMX’s, 12GB

## Slide 4: MAXWELL/PASCAL CC5.2, CC6.1 SM
“SMM” (enhanced SM)
128 SP units (“cores”)
4 DP units
LD/ST units
cc 6.1: INT8
4 warp schedulers
Each warp scheduler is dual-issue capable
M40: 24 SMM’s, 12/24GB
P40: 30 SM’s, 24GB
P4: 20 SM’s, 8GB

## Slide 5: PASCAL/VOLTA CC6.0/7.0
5
64 SP units (“cores”)
32 DP units
LD/ST units
FP16 @ 2x SP rate
cc7.0: TensorCore
P100/V100 2/4 warp schedulers
Volta adds separate int32 units
P100: 56 SM’s, 16GB
V100: 80 SM’s, 16/32GB

## Slide 6: EXECUTION MODEL
Software
Hardware
CUDA threads are executed by scalar processors (Lane of SIMD processor)
CUDA Thread
Scalar Processor
Thread Block
Streaming Multiprocessor
Thread blocks are split to warps and executed on multiprocessors (SIMD processor) in SIMT.
Several concurrent thread blocks can reside on one SIMD processor (when the number of thread blocks greater than multiprocessors) - limited by SIMD processor resources (shared memory and register file)
...
Grid
Device
A kernel is launched as a grid of thread blocks
Lane of SIMD processor
SIMD processor
Warp
SIMD thread

## Slide 7: WARPS
7
Thread Block
Streaming Multiprocessor
SIMD Processor
32 CUDA Threads
32 CUDA Threads
32 CUDA Threads
...
Warps
A thread block consists of thread warps
A warp is executed physically in parallel (SIMD) on a multiprocessor
=

## Slide 8: LAUNCH CONFIGURATION

## Slide 9: LAUNCH CONFIGURATION
Key to understanding:
Instructions are issued in order
A SIMD thread stalls when one of the operands isn’t ready:
Memory read by itself doesn’t stall execution
Latency is hidden by switching threads
GPU MEM latency: >100 cycles e.g. 100 (varies by architecture/design)
Arithmetic latency: <100 cycles e.g. 10 (varies by architecture/design)
How many threads/threadblocks to launch? Conclusion:
Need enough threads to hide latency

## Slide 10: LATENCY: ANALYSIS
Suspect unhidden latency if:
  Neither memory nor instruction throughput is close to HW theoretical rates
  Poor overlap between mem and math
    Full-kernel time is significantly larger than max{mem-only, math-only}
      Refer to SC10 or GTC10 Analysis-Driven Optimization slides for details
Two possible causes:
  Insufficient concurrent threads per SIMD processor to hide latency
    Occupancy too low
    Too few threads in kernel launch to load the GPU
      elapsed time doesn’t change if problem size is increased (and with it the number of blocks/threads)
  Too few concurrent threadblocks per SIMD processor when using syncthreads()
    syncthreads() can prevent overlap between compute and mem within the same threadblock

## Slide 11: SIMPLIFIED VIEW OF LATENCY AND SYNCS
Memory-only time Math-only time
Full-kernel time, one large threadblock per SIMD processor
Kernel where most math cannot be executed until all data is loaded by the threadblock
time

## Slide 12: SIMPLIFIED VIEW OF LATENCY AND SYNCS
Memory-only time Math-only time
Full-kernel time, two warps per SIMD processor (each half the size of one large one)
Full-kernel time, one warp per SIMD processor
Kernel where most math cannot be executed until all data is loaded by the threadblock
time

## Slide 13: GPU LATENCY HIDING
In CUDA C source code:
int idx = threadIdx.x+blockDim.x*blockIdx.x;
c[idx] = a[idx] * b[idx];
In machine code:
I0: LD R0, a[idx];
I1: LD R1, b[idx];
I2: MPY R2,R0,R1

## Slide 14: GPU LATENCY HIDING – INSIDE THE SM
I0: LD R0, a[idx];
I1: LD R1, b[idx];
I2: MPY R2,R0,R1
warps
W0:
W1:
W2:
W3:
W4:
W5:
W6:
W7:
W8:
W9:
…
clock cycles:
C0 C1 C2 C3 C4 C5 C6 C7 C8 C9 C10 C11 C12 C13 C14 C15 C16 C17 C18 …
More warps sequentially access data elements without overlapping.

## Slide 15: GPU LATENCY HIDING – INSIDE THE SM
I0 I1
warps
W0:
W1:
W2:
W3:
W4:
W5:
W6:
W7:
W8:
W9:
…
C0 C1 C2 C3 C4 C5 C6 C7 C8 C9 C10 C11 C12 C13 C14 C15 C16 C17 C18 …
I0: LD R0, a[idx];
I1: LD R1, b[idx];
I2: MPY R2,R0,R1
clock cycles:

## Slide 16: GPU LATENCY HIDING – INSIDE THE SM
I0 I1
warps
W0:
W1:
W2:
W3:
W4:
W5:
W6:
W7:
W8:
W9:
…
C0 C1 C2 C3 C4 C5 C6 C7 C8 C9 C10 C11 C12 C13 C14 C15 C16 C17 C18 …
I0: LD R0, a[idx];
I1: LD R1, b[idx];
I2: MPY R2,R0,R1
clock cycles:

## Slide 17: GPU LATENCY HIDING – INSIDE THE SM
I0 I1
I0
warps
W0:
W1:
W2:
W3:
W4:
W5:
W6:
W7:
W8:
W9:
…
C0 C1 C2 C3 C4 C5 C6 C7 C8 C9 C10 C11 C12 C13 C14 C15 C16 C17 C18 …
I0: LD R0, a[idx];
I1: LD R1, b[idx];
I2: MPY R2,R0,R1
clock cycles:

## Slide 18: GPU LATENCY HIDING – INSIDE THE SM
I0 I1
I1
I0
warps
W0:
W1:
W2:
W3:
W4:
W5:
W6:
W7:
W8:
W9:
…
C0 C1 C2 C3 C4 C5 C6 C7 C8 C9 C10 C11 C12 C13 C14 C15 C16 C17 C18 …
I0: LD R0, a[idx];
I1: LD R1, b[idx];
I2: MPY R2,R0,R1
clock cycles:

## Slide 19: GPU LATENCY HIDING – INSIDE THE SM
I0 I1
I1
I0
I1
I0
warps
W0:
W1:
W2:
W3:
W4:
W5:
W6:
W7:
W8:
W9:
…
C0 C1 C2 C3 C4 C5 C6 C7 C8 C9 C10 C11 C12 C13 C14 C15 C16 C17 C18 …
I0: LD R0, a[idx];
I1: LD R1, b[idx];
I2: MPY R2,R0,R1
clock cycles:

## Slide 20: GPU LATENCY HIDING – INSIDE THE SM
I0 I1
I1
I0
I1
I0
I0 I1
I0 I1
I1
I0
I1
I0
I0 I1
warps
W0:
W1:
W2:
W3:
W4:
W5:
W6:
W7:
W8:
W9:
…
C0 C1 C2 C3 C4 C5 C6 C7 C8 C9 C10 C11 C12 C13 C14 C15 C16 C17 C18 …
Warps scheduled by a thread scheduler
I0: LD R0, a[idx];
I1: LD R1, b[idx];
I2: MPY R2,R0,R1
clock cycles:

## Slide 21: GPU LATENCY HIDING – INSIDE THE SM
I1
I0
I1
I0
I0 I1
I0 I1
I1
I0
I1
I0
I0 I1
I0 I1
I0 I1
warps
W0:
W1:
W2:
W3:
W4:
W5:
W6:
W7:
W8:
W9:
…
C0 C1 C2 C3 C4 C5 C6 C7 C8 C9 C10 C11 C12 C13 C14 C15 C16 C17 C18 …
I0: LD R0, a[idx];
I1: LD R1, b[idx];
I2: MPY R2,R0,R1
clock cycles:

## Slide 22: GPU LATENCY HIDING – INSIDE THE SM
I1
I0
I0 I1
I0 I1
I1
I0
I1
I0
I0 I1
I0 I1
I0 I1
I2
I0 I1
warps
W0:
W1:
W2:
W3:
W4:
W5:
W6:
W7:
W8:
W9:
…
C0 C1 C2 C3 C4 C5 C6 C7 C8 C9 C10 C11 C12 C13 C14 C15 C16 C17 C18 …
I0: LD R0, a[idx];
I1: LD R1, b[idx];
I2: MPY R2,R0,R1
clock cycles:

## Slide 23: GPU LATENCY HIDING – INSIDE THE SM
I1
I0
I0 I1
I0 I1
I1
I0
I1
I0
I0 I1
I0 I1
I0 I1
I2
I2
I0 I1
warps
W0:
W1:
W2:
W3:
W4:
W5:
W6:
W7:
W8:
W9:
…
C0 C1 C2 C3 C4 C5 C6 C7 C8 C9 C10 C11 C12 C13 C14 C15 C16 C17 C18 …
I0: LD R0, a[idx];
I1: LD R1, b[idx];
I2: MPY R2,R0,R1
clock cycles:

## Slide 24: LAUNCH CONFIGURATION
Hiding arithmetic latency:
Need ~10’s warps (~320 CUDA threads, or 10 SIMD threads) per SIMD processor
Or, latency can also be hidden with independent instructions from the same warp
->if instructions never depends on the output of preceding instruction, then only 5 warps are needed, etc.
Maximizing global memory throughput:
Depends on the access pattern, and word size
Need enough memory transactions in flight to saturate the bus
Independent loads and stores from the same thread
Loads and stores from different threads
Larger word sizes can also help (float2 is twice the transactions of float, for example)

## Slide 25: MAXIMIZING MEMORY THROUGHPUT
22
Increment of an array of 64M elements
Two accesses per thread (load then store) - dependent, so really 1 access per thread at a time
theoretical bandwidth: ~120 GB/s
Several independent smaller accesses have the same effect as one larger one.
For example:
Four 32-bit ~= one 128-bit
(SIMD Processor)

## Slide 26: LAUNCH CONFIGURATION: SUMMARY
Need enough total threads to keep GPU busy
Typically, you’d like 512+ CUDA threads per SIMD Processor (aim for 2048 - maximum “occupancy”)
More if processing one fp32 element per thread
Of course, exceptions exist
Threadblock configuration
Threads per block should be a multiple of warp size (32)
SIMD Processor can concurrently execute at least 16 thread blocks (Maxwell/Pascal/Volta/Ampere: 32)
Really small thread blocks prevent achieving good occupancy
Really large thread blocks are less flexible
Could generally use 128-256 threads/block, but use whatever is best for the application

## Slide 27: ASIDE: WHAT IS OCCUPANCY?
A measure of the actual thread load in an SIMD Processor, vs. peak theoretical or peak achievable
CUDA includes an occupancy calculator spreadsheet
Achievable occupancy is affected by limiters to occupancy
Primary limiters:
Registers per thread (can be reported by the profiler, or can get at compile time)
Threads per threadblock
Shared memory usage

## Slide 28: SUMMARY
GPU is a massively thread-parallel, latency hiding machine
Kernel Launch Configuration:
Launch enough threads per SM to hide latency
Launch enough threadblocks to load the GPU
Use analysis/profiling when optimizing:
“Analysis-driven Optimization” (future session)
-> Nsight Compute can show you information about whether you’ve saturated the compute subsystem or the memory subsystem.

## Slide 29: FUTURE SESSIONS
Fundamental Optimization, Part 2
Atomics, Reductions, Warp
Shuffle Using Managed Memory
Concurrency (streams, copy/compute overlap, multi-
GPU) Analysis Driven Optimization
Cooperative Groups

## Slide 30: FURTHER STUDY
Optimization in-depth:
http://on-demand.gputechconf.com/gtc/2013/presentations/S3466-Programming-Guidelines- GPU-Architecture.pdf
Analysis-Driven Optimization:
http://on-demand.gputechconf.com/gtc/2012/presentations/S0514-GTC2012-GPU-Performance- Analysis.pdf
CUDA Best Practices Guide:
https://docs.nvidia.com/cuda/cuda-c-best-practices-guide/index.html
CUDA Tuning Guides:
https://docs.nvidia.com/cuda/index.html#programming-guides (Kepler/Maxwell/Pascal/Volta)